## Slide 1: Cuffless estimation of blood pressure from PPG signals using Transformers
Arijit Bhattacharyya
Supervisors: Dr Zaibaa Patel, Professor Esther Rodriguez Villegas
Second marker: Dr Christos Bouganis
27/06/2022

## Slide 2: Contents
Background
Analysis and design of the system
Proposed Model (Demonstration)
Results
Conclusion

## Slide 3: Blood Pressure
Blood Pressure Category | Systolic Blood Pressure (mmHg) | AND/OR | Diastolic Blood Pressure (mmHg)
Hypotension | ≤ 90 | OR | ≤ 60
Normal | 90-120 | AND | 60-80
Prehypertension | 121-139 | OR | 81-89
Stage 1 Hypertension | 140-159 | OR | 90-99
Stage 2 Hypertension | ≥ 160 | OR | ≥ 100
Ludi Wang et al. “A novel neural network model for blood pressure estimation using photoplethesmography without electrocardiogram”. In: Journal of Healthcare Engineering 2018 (2018). issn: 20402309. doi: 10.1155/2018/7804243

## Slide 4: Continuous Blood Pressure monitoring
Invasive
  Limited to clinical environments (e.g in ICU)
  Discomfort
  May cause complications
Non-invasive
  Cumbersome due to repeated inflation and deflation
  Inaccurate
  Not feasible for long term monitoring
A better method is required!
https://doctorlib.info/physiology/medical/96.html
https://www.tctmd.com/news/cuff-bp-more-variable-intra-arterial-measures

## Slide 5: Continuous Blood Pressure monitoring
Wearables
  Several existing smart watch models:
    Aktiia
    Heartisans BP smartwatch
    BPro, developed by HealthSTATS Technologies
  Still inaccurate
  Potential for use in long term BP monitoring
  Face power limitations, important to consider:
    Maximising accuracy
    Minimising computational complexity
https://aktiia.com/uk/

## Slide 6: Aims
Develop a novel algorithm in software to perform cuffless estimation of blood pressure values using PPG signals
Algorithm should aim to:
  Maximise prediction accuracy
  Minimise computational complexity

## Slide 7: Pipeline for Cuffless BP estimation from PPG

## Slide 8: Photoplethysmography (PPG)
An optically obtained signal that can be used to detect blood volume changes
Measured noninvasively
Potential to be used in future wearable technologies
https://en.wikipedia.org/wiki/Photoplethysmogram

## Slide 9: Photoplethysmography (PPG)
Contains information on cardiovascular parameters such as BP
Has high correlation with BP in both the time and frequency domains

## Slide 10: Database
Multiparameter Intelligent Monitoring in Intensive Care (MIMIC) database
  PPG and correspondent arterial BP signals
  Data taken from 72 ICU patients
Data divided into 1-second windows

## Slide 11: Dataset Noise
Signals in this dataset often contain significant artifacts
  Physiologically improbable BP values
  Improbable Normal-to-Normal (NN) intervals
  Improbable heart rate values
  Noisy PPG and BP signals (low frequency noise and baseline wandering)
Strong preprocessing is required

## Slide 12: Preprocessing Steps
Remove unreliable patients and their data
Remove outliers
Z-score normalisation
4th order Butterworth bandpass filter

## Slide 13: Preprocessed Dataset
- ~ 340,000 1-second windows from 12 different patients

## Slide 14: Families of Neural networks
Review of literature resulted in 3 families:
Convolutional Neural Networks (CNNs)
Long Short Term Memory Recurrent Neural Networks (LSTM-RNNs)
Transformers using the Attention mechanism

## Slide 15: Handpicked vs Automated Feature extraction
PPG
Handpicked Features
SVM
Bi-LSTM, Bi-GRU
Automated Feature Extraction
CNNs
RNNs
Transformer Encoder
AlexNet
Bi-LSTM
Attention
Auto-encoder
ResNet

## Slide 16: Transformers
Advantageous over CNNs and RNNs with large data inputs
Main components:
Layer Normalisation
Multi head Self Attention Mechanism
Feed forward neural network
Several parameters required to set up the network:
Head size, number of heads, number of convolutional filters, number of encoder blocks
Ashish Vaswani et al. Attention Is All You Need. 2017. doi: 10.48550/ARXIV.1706. 03762. url: https://arxiv.org/abs/1706.03762

## Slide 17: Proposed Transformer Encoder Architecture

## Slide 18: Results
Neural Network Architecture | SBP MAE (mmHg) |  | DBP MAE (mmHg) | 
 | Training | Validation | Training | Validation
AlexNet | 4.5867 / 2.0134 | 4.6724/6.7865 | 3.5892/1.3424 | 3.7895/2.9451
ResNet | 7.7123/1.9845 | 9.8753/6.9732 | 6.0123/1.2765 | 10.297/2.2145
ST ResNet | 7.5329/7.4923 | 9.4234/9.5246 | 4.2154/3.7894 | 4.3785/3.9720
Bi-LSTM | 5.1370/5.1299 | 8.2793/8.2432 | 3.2159/3.7913 | 3.4196/3.5217
Transformer Encoder | 13.214/12.992 | 13/359/12.740 | 6.3412/6.4387 | 5.6129/5.4763
For each cell:
- (Result without PPG derivatives) / (Result with PPG derivatives)

## Slide 19
Chart: Training and Validation performance with no PPG derivative
| Training SBP | Validation SBP | Training DBP | Validation DBP
AlexNet | 4.5867 | 4.6724 | 3.5892 | 3.7895
ResNet | 7.7123 | 9.8753 | 6.0123 | 10.297
ST ResNet | 7.5329 | 9.4234 | 4.2154 | 4.3785
Bi-LSTM | 5.137 | 8.2793 | 3.2159 | 3.4196
Transformer Encoder | 13.214 | 13.359 | 6.3412 | 5.6129

## Slide 20
Chart: Training and Validation performance with PPG derivatives
| Training SBP | Validation SBP | Training DBP | Validation DBP
AlexNet | 2.0134 | 6.7865 | 1.3424 | 2.9451
ResNet | 1.9845 | 6.9732 | 1.2765 | 2.2145
ST ResNet | 7.4923 | 9.5246 | 3.7894 | 3.972
Bi-LSTM | 5.1299 | 8.2432 | 3.7913 | 3.5217
Transformer Encoder | 12.992 | 12.74 | 3.5217 | 5.4763

## Slide 21: Results
Neural Network Architecture | Inference Time (ms per test sample)
AlexNet | 0.5204
ResNet | 0.5756
ST ResNet | 0.5891
Bi-LSTM | 0.6043
Transformer Encoder | 0.3590
Chart: Inference Time
| AlexNet | ResNet | ST ResNet | Bi-LSTM | Transformer Encoder
Inference Time (ms per test sample) | 0.5204 | 0.5756 | 0.5891 | 0.6043 | 0.359

## Slide 22: Conclusion
Two variants of the Transformer encoder technique have been proposed
  First technique: Standard Transformer Encoder
  Second technique: Addition of 1st and 2nd order derivatives of PPG
  Compared against two other neural network families (CNNs, LSTMs)
Trained on a large dataset after extensive pre-processing
  Further data required to compare with health standards
Potential to be used in future BP monitoring devices after further testing

## Slide 23: Thank you for listening